## Slide 1
SECURING THE DIGITAL MINE
A Metaheuristic-Optimized Deep Learning Framework for Edge Intrusion Detection in IoT-Enabled Mineral Operations
RUSSIAN-AFRICAN FORUM-CONTEST OF YOUNG SCIENTISTS 2026 | TRACK 3: SMART SUBSOIL Under the Auspices of UNESCO | Empress Catherine II Saint Petersburg Mining University
John Okyere (Lead) • Ezekeil Baah • Clement Baffour • Parker Paa Annobil • George Akwesi Bonnah Department of ICT, University of Education, Winneba & Kayaba Labs | hello@johnokyere.xyz
1. PROBLEM & INDUSTRIAL CONTEXT
• Digital Subsoil Transformation: African and Russian mines are rapidly deploying IoT sensors, autonomous haulage, and SCADA telemetry to optimize ore yield.
• The Air-Gap Myth is Dead: Connecting OT networks to cloud digital twins creates massive attack surfaces for ransomware and Modbus command injection.
• Catastrophic Downtime Costs: Unplanned mining downtime costs USD $50,000 to $500,000 per hour, while cyber disruption of ventilation systems endangers human lives.
• Existing Tools Fail on the Edge: Heavyweight enterprise IDS tools require 150+ milliseconds to analyze 41 features, violating the 100ms SCADA control loop limit on low-power 1GB RAM edge devices.
2. 4-LAYER SYSTEM ARCHITECTURE
A complete edge-to-cloud security pipeline combining metaheuristic feature pruning with spatial-temporal deep learning:
3. EXPERIMENTAL BENCHMARK RESULTS
✓ 75.61% Data Pruning: BWOA reduces 41 features down to 10 optimal dimensions while maintaining 92.31% Random Forest CV validation accuracy.
✓ 70.56% Multi-Class Accuracy: Tested on 22,544 held-out NSL-KDD samples with 96.89% precision on Normal traffic and 89.04% recall on DoS attacks.
✓ 0.76ms Edge Latency: Float16 quantized model executes 207x faster than baseline, easily passing the sub-100ms industrial SCADA constraint.
4. EDGE HARDWARE DEPLOYMENT
Validated on Raspberry Pi 4B (1GB RAM) edge hardware for remote subsoil facilities:
0.76 ms
Inference Latency (Target: < 100 ms)
0.82 MB
Model Memory Size (83.2% Compression)
290 MB
Peak RAM Usage (Fits 1GB Pi Gateway)
2.5 W
Power Consumption (Solar/Battery Ready)
5. ECONOMIC ROI & UN SDG IMPACT
★ SDG 9: Industry, Innovation & Infrastructure Hardens critical mining cyber-physical systems against zero-day disruption, safeguarding essential mineral supply chains.
★ SDG 8: Decent Work & Economic Growth Protects underground worker safety by preventing cyber manipulation of toxic gas sensors and ventilation grids.
★ SDG 17: Partnerships for the Goals Fosters bilateral Russian-African scientific collaboration, knowledge transfer, and open-source capacity building.
★ High Economic ROI (200x - 300x) Preventing a single 24-hour ransomware outage on a ball mill or autonomous truck saves $300k to $450k, against an annual deployment cost of under $1,500.
6. CONCLUSION & OPEN SOURCE ARTIFACTS
► Complete Open-Source Ecosystem: Full code, training notebooks, benchmarks, and 75 unit test suites are fully open source on GitHub.
► NPM Edge Sniffer Package: Install instantly on any gateway via '@mhiskall282/unesco-mine-sec-cli' from GitHub Packages.
► UNESCO Forum Delegation: Presented by the University of Education, Winneba & Kayaba Labs research team at Empress Catherine II Saint Petersburg Mining University.
► Repository URL: https://github.com/mhiskall282/Securing-the-Digital-Mine-UNESCO-Project
► Correspondence Email: hello@johnokyere.xyz | Portfolio: https://johnokyere.xyz